## Slide 1: Uncertainty in Measurement
How would you measure 9 ml most precisely?
What is the volume being measured here?
What is the uncertainty measurement?
For analog measurements, the uncertainty is + half the smallest scale division.

## Slide 2
For a digital scale, the uncertainty is + the smallest scale division.

## Slide 3
A measurement always has some degree of uncertainty.

## Slide 4: Uncertainty in Measurement
Different people estimate differently.
Record all certain numbers and one estimated number.

## Slide 5: Significant figures
A significant figure represents an actual measurement
A measurement of all the digits known with certainty, plus one that is estimated or uncertain

## Slide 6: Significant Figures
Significant figures are the meaningful figures in our measurements and they allow us to generate meaningful conclusions
Numbers recorded in a measurement are significant.
  All the certain numbers plus first estimated number
  e.g. 2.85 cm
We need to be able to combine data and still produce meaningful information
There are rules about combining data that depend on how many significant figures we start with………

## Slide 7: Significant Figures
  Rules for Counting Significant Figures
Nonzero integers always count as significant figures.
1457 has 4 significant figures
23.3 has 3 significant figures

## Slide 8: Significant figures
  Leading zeros - never count 0.0025 2 significant figures
  Captive zeros - always count 1.008 4 significant figures
  Trailing zeros - count only if the number is written with a decimal point 100 1 significant figure 100. 3 significant figures 120.0 4 significant figures

## Slide 9
Exact numbers - unlimited significant figures
Not obtained by measurement
  Determined by counting: 3 apples
  Determined by definition: 1 in. = 2.54 cm

## Slide 10: How Many Significant Figures?
1422
65,321
1.004 x 105
200
435.662
50.041
102
102.0
1.02
0.00102
0.10200
1.02 x 104
1.020 x 104
60 minutes in an hour
500 laps in the race

## Slide 12: Rules for Multiplication and Division
I measure the sides of a rectangle, using a ruler as 4.51cm and 9.32cm
What does a calculator tell me the area is?
What is the range of areas that my measurements might indicate (consider the range of lengths that my original measurements might cover)?

## Slide 13
The number of significant figures in the result is the same as in the measurement with the smallest number of significant figures.

## Slide 14: Rules for Addition and Subtraction
The number of significant figures in the result is the same as in the measurement with the smallest number of decimal places.

## Slide 15: Calculate the following. Give your answer to the correct number of significant figures and use the correct units
11.7 km x 15.02 km =
12 mm x 34 mm x 9.445 mm =
14.05 m / 7 s =
108 kg / 550 m3 =
23.2 L + 14 L =
55.3 s + 11.799 s =
16.37 cm – 4.2 cm =
350.55 km – 234.348 km =

## Slide 16: Random Errors
Caused by:
The readability of the measuring instrument
The effects of changes in surroundings that cannot be controlled
Random errors can be reduced by repeating the measurements.

## Slide 17: Systematic errors
Are the result of poor experimental design. Cannot be improved by repetition.

## Slide 18: Accuracy
How close a reading is to the true value.
The smaller the systematic error, the greater the accuracy

## Slide 19: Precision
Precision is how consistent the results are.
The smaller the random error the more precise the results.

## Slide 20: Propagation of Uncertainties
When adding or subtracting the uncertainty is the sum of the absolute uncertainties.
Ex:

## Slide 21: Multiplication and division
When multiplying or dividing, you must calculate the percent uncertainty, then add the percentages. This can be converted to the absolute value.